## Slide 1: VENTILATOR BASICS + NIPPV, Capnography, Vent settings & complications
EM/CC LECTURE SERIES
KIMBERLY PISTELL, DO
LT, MC, USN
NMCP EMERGENCY MEDICINE PGY4

## Slide 2: OUTLINE
Oxygenation
Ventilation
Breath types
Modes
Noninvasive
CPAP vs BiPAP
HiFLO
Ventilator terminology
Waveform Capnography
Vent Settings: Approach
Troubleshooting
Complications
Push-dose pressors
Pulse Oximetry
Resources

## Slide 3: OUTLINE
There are many different ways to approach learning this topic.
I have set this lecture up to learn either from a ground-up approach or problem focused approach. Click on the an outline topic on the previous slide in presentation mode to jump to a section.

## Slide 4: BACKGROUND
NIPPV and mechanical ventilation help with
Oxygenation
Ventilation (CO2)
Muscle fatigue

## Slide 5: OXYGENATION
Oxygenation can be influenced by:
FiO2
Mean Airway Pressure (MAP)
  1. Why increasing PEEP helps improve oxygenation- you are increasing the area under the curve
  2. Can also increase Itime
2
1

## Slide 6: VENTILATION
Ventilation refers to the removal of CO2
Increase CO2 removal = minute ventilation = RR and tidal volume
Minute Ventilation = RR x Vt

## Slide 7: TYPES OF BREATHS
Controlled: Breaths only delivered at a rate you set-vent does ALL the work
Assisted: Patient initiated breaths-vent dose ALL of the work
Supported: Patient initiated breath-vent provides SOME of the work
Volume: A set volume is delivered at whatever pressure is required
  Cons: uncomfortable/not physiologic, may require too high of pressures
Pressure: A set pressure over time provides whatever volume your lung compliance allows
  Pro: more physiologic/comfortable
  Cons: may not achieve adequate volumes

## Slide 8: MODES
Volume Assist Control (AC): You set the volume (typically 6-8cc/kg), RR, FiO2, PEEP
  Assist = if patient triggers a breath faster than your set rate, they will receive the preset volume
Pressure Assist Control (AC): You set the pressure on top of the PEEP (targeting normal Vt) RR, FiO2
  Assist = if patient triggers a breath faster than your set rate, they will receive the preset pressure over the set Itime
Pressure Support (PS): You set a pressure-that’s it, similar to CPAP. This mode is typically used during SBT (spontaneous breathing trial). Patient initiates every breath and receives the set pressure. (~ 5 cmH2O)

## Slide 9: MODES
Synchronized Mandatory Ventilation (SIMV) + PS: Combines all 3 modes. You set RR, FiO2, PEEP
  Volume/Pressure control: you set the volume/pressure which will be given at a set rate if the patient does not trigger a breath. The machine will provide an ASSISTED breath (machine still does the work) if the patient triggers a breath around the set rate. If they trigger a breath in between the set rate breaths, then they will receive a SUPPORTED breath with a preset pressure.
Pressure Regulated Volume Control (PRVC): You set Vt. Breaths can be controlled or assisted.
  The machine calculates the patient’s lung compliance and delivers the set Vt at the lowest possible pressure. If compliance decreases, then more pressure is needed to achieve the set tidal volume.
SIMV/PRVC + PS: typically seen in the PICU.
  You set the Vt, RR, FiO2, PEEP, and PS (pressure support)
  The machine will deliver pressure regulated breaths at a set rate based on lung compliance to achieve a set Vt and will provide pressure supported breaths if triggered in between the set rate

## Slide 10: MODES
Airway Pressure Release Ventilation
“elevated CPAP” allows for alveoli recruitment and gas exchange
Open exhalation valve allows for spontaneous breathing dur Thigh
Used typically for ARDS (esp COVID)
Initial settings:
  Phigh ~ 30, Plow 0, Thigh 5-6 sec, Tlow 0.5 sec
https://resusreview.com/2013/aprv-ventilation-mode-introduction-basic-use-management-and-advanced-tips/

## Slide 11: TYPES
Noninvasive
  CPAP
  BiPAP
  HFNC
Invasive
  Intubation
  Cricothyrotomy
https://emcrit.org/ibcc/support/

## Slide 12: NONINVASIVE
Indications:
- Respiratory support in an awake, stable, patient able to clear secretions without active vomiting or immediate risk for cognitive decline
Prevent respiratory muscle fatigue
Diseases:
COPD/Asthma
CHF
Neuromuscular disease
Contraindications:
Multiorgan failure
Vomiting
Facial trauma
Copious secretions
Depressed mental status
Uncooperative

## Slide 13: NONINVASIVE
CPAP
Increase mean airway pressure (MAP) and oxygenation
  Good for hypoxemic respiratory failure
Useful when all you need is increased airway pressure (CHF)
Consistently reproduced benefits with acute cardiogenic pulmonary edema
BiPAP
Driving pressure (delta) and mechanical support
Good for hypoxemic or hypercarbic respiratory failure
   Both oxygenation & ventilation
    Neuromuscular weakness
    Obesity
Increase oxygenation
Increase FiO2
Increase MAP
Increase ventilation
- Increase delta

## Slide 14: NONINVASIVE: CHF
Increased mean airway pressure reduces preload and afterload
CPAP: one pressure  increases mean Airway pressure
BiPAP: expiratory pressure increases mean airway pressure
- Driving pressure (delta) = IPAP – EPAP, affects minute ventilation
  Large delta not needed in CHF, high expiratory pressures are
To titrate: Increase EPAP but keep delta the same when making adjustments
  EX: start 10/5, delta 5; increase to 18/13, delta 5
 Why both CPAP or BiPAP work for CHF!!

## Slide 15: NONINVASIVE: COPD/ASTHMA
BiPAP
Benefits from driving pressure (delta), especially if they are experiencing respiratory fatigue
   Increasing delta P increases minute ventilation by increasing your Vt
To Titrate, increase delta P
  Ex) start 10/5, delta 5; increase 15/8, delta 7

## Slide 16: NONINVASIVE: NEUROMUSCULAR
Goal is to support with minute ventilation with Vt ,not mean airway pressure
Need Driving Pressure, aka Delta P  BiPAP
Start with low setting EPAP and IPAP, and increase your delta as needed
  EX: start 10/5, delta 5; increase to 15/5, delta 10

## Slide 17: NONINVASIVE: HiFlo
HFNC: warmed, humidified air at rate up to ~ 60 L/min
Benefits:
Some PEEP
Up to 100% FiO2
CO2 washout reduces anatomic dead space  improves ventilation
Better tolerated than BiPAP

## Slide 18: NONINVASIVE: ALGORITHM

## Slide 19: Ventilator Settings

## Slide 20: VENTILATOR: DEFINITIONS
Control breaths: set interval breaths
Assisted breaths: patient-triggered, machine-delivers pre-set breath
Supported breaths: patient-triggered, machine-delivers supported breath
Peak Inspiratory Pressure (PIP): max pressure needed during inspiration to overcome resistance pressure (ET tube and large proximal airways) and elastic pressure of lungs (small airways and alveoli)
Plateau Pressure: pressure needed to overcome elastic forces
  High Pplat = compliance issues
  Obtained with end-inspiratory hold
https://rebelem.com/simplifying-mechanical-ventilation-part/

## Slide 21: VENTILATOR: DEFINITIONS
High PIP and Pplat = lung disease
High PIP, normal Pplat = inc airway resistance
https://rebelem.com/simplifying-mechanical-ventilation-part/
PIP- Pplat increased
PIP- Pplat same
Pplat same
Pplat increased
PIP
Pplat
Increased PIP
Increased PIP
Baseline
Inc resistance
Dec compliance
Pressure
Time

## Slide 22: VENTILATOR: CAPNOGRAPHY
http://www.emdocs.net/interpreting-waveform-capnography-pearls-and-pitfalls/
Always use capnography
Learn how to analyze
Shape
Height
Frequency
Baseline
Rhythm

## Slide 23: VENTILATOR: CAPNOGRAPHY
http://www.emdocs.net/interpreting-waveform-capnography-pearls-and-pitfalls/

## Slide 24: VENTILATOR: APPROACH
Lung protective = oxygenation issue
Obstructive disease = ventilation issue
Post-Intubation
Assess blood gas
Check vent pressures
Wean FiO2 down to < 60%

## Slide 25: VENTILATOR: LUNG PROTECIVE
ARDSNet 1994: study:1 of few trials to show mortality benefit with low-tidal-volume ventilation
ARDS: an inflammatory lung condition involving both lungs that may complicate severe pneumonia, trauma, sepsis, aspiration of gastric contents, and many other conditions
The injured lung should be managed gently with small breaths and low pressures from the ventilator.
Conservative use of intravenous fluids combined with removal of excess fluids with diuretics
http://www.ardsnet.org/

## Slide 26: VENTILATOR: LUNG PROTECIVE

## Slide 27: VENTILATOR: LUNG PROTECIVE
http://www.ardsnet.org/

## Slide 28: VENTILATOR: LUNG INJURY
Volume Assist/Control
- 5 settings:
  Tidal volume: start with 8 mL/kg PBW (alveolar protection)
  RR: initial 16 bpm, adjust to achieve PaCO2 goal
    Increase rates with severe acidosis (DKA, ASA) see next slide
  PEEP: initial 5 cmH2O, increase for improved oxygenation
  FiO2: initial 100%, titrate down
  Flow: initial 60 L/min (patient comfort)
Check blood gas 20-30 minutes after

## Slide 29: VENTILATOR: METABOLIC ACIDOSIS
Inadequate compensation
 cardiac arrest!!!
https://rebelem.com/simplifying-mechanical-ventilation-part-3-severe-metabolic-acidosis/
1. Calculate goal PaCO2 using Winter’s formula
  Goal C02 = 1.5 X HCO3+ 8 (+/- 2)
2. Use the table to get a rough estimate for minute ventilation
3. Check blood gas after 20-30 minutes

## Slide 30: VENTILATOR:CHECK PRESSURES
Peak Pressure: alveolar pressure + large airway + ventilator equipment
Plateau Pressure: pressure in alveoli, during inspiratory hold
Goal < 30 cm
  If elevated, decrease tidal volume (= alveolar protection), not PEEP
https://www.emra.org/emresident/article/demystifying_ventilator_alarms/

## Slide 31: VENTILATOR: OBSTRUCTIVE DISEASE
Volumes Assist/Control
5 Settings
  Tidal volume: same 6 - 8 mL/kg PBW
  RR: initial 8-10 bpm, lower to allow longer time expiration
    Permissible hypercapnia
  PEEP: low < 5, (oxygenation is not the issue)
  FiO2: low 40%, (oxygenation is not the issue)
  Flow: initial 60-80 mL/min, may need to adjust I:E ratio 1:4 or 1:5

## Slide 32: VENTILATOR:CHECK PRESSURES
Peak Pressure: will be elevated due to obstructive disease; alveolar pressure + large airway + ventilator equipment
  - Increase vent alarm settings for Peak Pressure
Plateau Pressure: should remain < 30; pressure in alveoli, during inspiratory hold
  - If elevated- decrease respiratory rate, increase inspiratory flow rate, decrease I:E
https://www.emra.org/emresident/article/demystifying_ventilator_alarms/

## Slide 33: VENTILATOR: VOLUME ASSIST/CONTROL
Disadvantages:
Cannot match natural inspiratory flow pattern (constant flow rate)
  Decreased patient comfort  add sedation
Less control over peak inspiratory pressures

## Slide 34: VENTILATOR: PRESSURE ASSIST/CONTROL
Pressure Assist/Control
- Constant pressure with variable decelerating inspiratory flow
Advantage: patient comfort, greater control over pressure
Disadvantage: less control over minute ventilation (Tv x RR)

## Slide 35: VENTILATOR: TROUBLESHOOTING
Persistent hypoxemia
Intubate with 100% Fi02, then quickly wean to < 60%
Consider interventions if unable to titrate < 60% after a few hours
  Treat/identify underlying cause
  Increase PEEP
  Paralysis
  Prone positioning
  ECMO

## Slide 36: VENTILATOR: PERSISTENT HYPOXEMIA

## Slide 37: VENTILATOR: TROUBLESHOOTING
DOPESS
Dislodgement: too shallow/deep
  Check tube depth (3 X tube size)
  Caution with increasing depth if too shallow. Recommend visualizing with laryngoscope.
Obstruction: mucus, biting, kinked tube, bronchospasm
  Pass a suction catheter through?
  Increase paralysis if biting
Pneumothorax:
  Visualize lung sliding on ultrasound?
Equipment failure: leak
  Check entire circuit-cuff to vent
Stacking (breath): check flow curves
  Does the flow curve reach 0?
    No  Disconnect vent
Synchrony: erratic breathing
  Increase sedation/paralysis

## Slide 38: VENTILATOR: COMPLICATIONS
Ventilator Induced Lung Injury
  Barotrauma
  Atelectotrauma
  O2 toxicity
Hemodynamics
  Decreased preload
  Increased RV afterload
  Decreased LV afterload
Acidosis
Preoxygenate
&
Resuscitate before intubate!!!
HOp Killers
Hypotension, hypOxemia, pH

## Slide 39: VENTILATOR: HYPOTENSION
Pre-intubation hypotension < 90 risk factor for cardiac arrest
IVF bolus
Pressors/”Boom Stick”
Caution in acute RV failure
Vasoactive meds | PVR/SVR | Right HF
Norepinephrine | +/- | OK
Epinephrine |  | Good
Vasopressin |  | Good
Phenylephrine |  | Bad
Pulmonary vascular resistance
Systemic vascular resistance
Increases pulmonary vascular resistance
**Works better than other pressors at low pH**

## Slide 40: VENTILATOR: PUSH-DOSE PRESSORS
1 mL + 9 mL  10 mcg/mL
1 mL + 100 mL  100 mcg/mL

## Slide 41: VENTILATOR: HYPOTENSION
RSI meds
Induction agents can drop BP by decreasing vascular tone and reducing venous return as well as sympathetic tone with some (benzos, propofol)
Preferred: ROCKETamine - low-dose ketamine and high dose rocuronium
  Ketamine- sympathetic surge, 0.5-1mg/kg
  Rocuronium 1-1.6 mg/kg

## Slide 42: VENTILATOR: ACIDOSIS
Mechanism:
Apnea during intubation increases CO2  worsening acidemia
Bicarb (HCO3) converts to CO2 and H2O  increased CO2 levels  worsening acidemia
Recommendations
Try to avoid intubation in the severe acidotic patient
Bicarb therapy- controversial. No studies have shown proven benefit when given pre-intubation for the severely acidotic.

## Slide 43: PULSE OXIMETRY
Pulse oximetry is based on the principle that O2Hb and HHb (deoxygenated Hb) absorb red and near-infrared (IR) light differentially.
Pulse oximeters emit 2 wavelengths: red at 660 nm and near-IR at 940 nm.
The relative amount of red and IR light absorbed are used by the pulse oximeter to ultimately determine the proportion of Hb bound to oxygen using a calibration curve factor.

## Slide 44: PULSE OXIMETRY
A microprocessor uses a ratio (calculated over a series of pulses) to determine the SpO2 based on a calibration curve that was generated empirically by measuring healthy volunteers whose saturations were altered from 100% to approximately 70%
O2Hb and COHb absorb red light similarly. COHb absorbs very little near-IR.
 Standard pulse oximeters that only emit red and near-IR light cannot differentiate between O2Hb and COHb.

## Slide 45: PULSE OXIMETRY
MetHb absorbs both red and IR light equally well.
 High MetHb levels result in an SpO2 of 80–85%.

## Slide 46: VENTILATOR RESOURCES
REBEL EM: https://rebelem.com/simplifying-mechanical-ventilation-part/
EMCrit Push-dose pressors: https://emcrit.org/emcrit/bolus-dose-pressors/
Emdocs Capnography: http://www.emdocs.net/interpreting-waveform-capnography-pearls-and-pitfalls/
Resus Review APRV: https://resusreview.com/2013/aprv-ventilation-mode-introduction-basic-use-management-and-advanced-tips/
ARDSnet: http://www.ardsnet.org/